## Slide 1: SLAM: Using Perception Systems

## Slide 2: Agenda
What is my thesis about?
What have I done until now?
My contribution to SOTA.
What to be done in remaining time?
DEMO
Questions/Suggestions.

## Slide 3: What is my thesis about?
SLAM: Simultaneous Localization and Mapping
Sensors:
    Proprioceptive sensors: Wheel Encoders, IMU
    Exteroceptive sensors: Camera and/or LIDAR and GPS
Ability to localize itself in an unknown environment
Simultaneously map the surrounding

## Slide 4: Why we need SLAM?
Localization is required to know the present state of the machine so that path-planning can be performed.
Sensors are noisy and inaccurate.
Inaccuracy starts getting accumulated as machine moves.
We need a correction step which can reset this accumulation from time to time.
Looking at the outside world and update/correct your state is what SLAM do.

## Slide 5: What have I done until now?
Extended Kalman Filter(EKF) SLAM:
        Utilizes gaussian distribution for representing uncertainty of the state
        Computes covariance matrix
        Need to know the starting location.
        Have prediction and correction step.
FAST SLAM a.k.a. Particle Filter SLAM:
        Assumes multiple random location of machine
        As machine move forward, landmarks assignment will reject most of the location
        No need to know the starting location.
        Have prediction and correction step.

## Slide 6: DEMO

## Slide 7: My contribution to SOTA.
Prediction
Correction

## Slide 8: Dead Reckoning to Alive Reckoning
Alive Reckoning using Heuristics:
  Utilizes 5 previous values.
  Utilizes inertia.
  -19.36% reduction in error

## Slide 9: Dead Reckoning to Alive Reckoning
Alive Reckoning using Multi Layer Perceptron(Regression):
    Utilizes 5 previous values of ground truth as input.
    Utilizes 1 future value of ground truth as output.
    Aim is to train model with ground truth data and run it live with real data.
    Not able to reduce much error.

## Slide 10: What to be done in remaining time?
Real time data using stereo camera, IMU and GPS: Visual SLAM
        Visual Odometry instead of wheel odometry
        IMU as Proprioceptive sensor
        GPS and Camera as Exteroceptive sensor
DEMO from CARLA simulator

## Slide 11: Questions/Suggestions.